## Slide 1
Multiple Sources
Blended Acquisition

## Slide 2: Polarcus’s Multiple-Source Initiative
“blended acquisition” with multiple sources
novel acquisition designs, and more data with the same quality

## Slide 3: Blended Acquisition
more rapidly firing of shots with overlapping shot records
novel acquisition designs, and more data with the same quality
Notes: firing shots in rapid succession, more rapidly than in a conventional acquisition, such that the respective shot records overlap, and leaving de-blending, that is the separation into individual shot records, to processing.
Here, you see two shot records, a green and an orange one, where the orange shot has been fired too “early” in conventional terms; the orange shot record overlaps with the green one.

## Slide 4: De-Blending
“blended” = continuous
shot record
Notes: With a succession of shots we get one big continuous shot record.
Blended data are, then, “de-blended”,

## Slide 5: De-Blending
“blended” = continuous
shot record
other domain
target shot
aligned
Notes: In order to de-blend the two shot records, firstly, we sort all the data into another domain, be it a common-midpoint, common-offset or other domain. Key point being, we sort the data such that the events of the green shot record align; then, because of the dithering of the shot times, the events of the orange shot record dis-align and appear as noise.
We strongly de-noise and assign remaining coherent energy to the green shot.
That coherent energy is removed from the original shot record.
Next, the remaining data are re-sorted such that the events of the orange shot record align; then, because of the dithering of the shot times, the events of the green shot record dis-align and appear as noise.
We strongly de-noise and assign remaining coherent energy to the orange shot.
This process is repeated several times, possibly in other domains, possibly with different de-noising tools.

## Slide 6: De-Blending
“blended” = continuous
shot record
other domain
noise shot
re-aligned
Notes: In order to de-blend the two shot records, firstly, we sort all the data into another domain, be it a common-midpoint, common-offset or other domain. Key point being, we sort the data such that the events of the green shot record align; then, because of the dithering of the shot times, the events of the orange shot record dis-align and appear as noise.
We strongly de-noise and assign remaining coherent energy to the green shot.
That coherent energy is removed from the original shot record.
Next, the remaining data are re-sorted such that the events of the orange shot record align; then, because of the dithering of the shot times, the events of the green shot record dis-align and appear as noise.
We strongly de-noise and assign remaining coherent energy to the orange shot.
This process is repeated several times, possibly in other domains, possibly with different de-noising tools.

## Slide 7: De-Blending
“blended” = continuous
shot record
other domain
Cadzow
filtered
Notes: In order to de-blend the two shot records, firstly, we sort all the data into another domain, be it a common-midpoint, common-offset or other domain. Key point being, we sort the data such that the events of the green shot record align; then, because of the dithering of the shot times, the events of the orange shot record dis-align and appear as noise.
We strongly de-noise and assign remaining coherent energy to the green shot.
That coherent energy is removed from the original shot record.
Next, the remaining data are re-sorted such that the events of the orange shot record align; then, because of the dithering of the shot times, the events of the green shot record dis-align and appear as noise.
We strongly de-noise and assign remaining coherent energy to the orange shot.
This process is repeated several times, possibly in other domains, possibly with different de-noising tools.

## Slide 8: De-Blending
“blended” = continuous
shot record
other domain
target shot
aligned
noise model
Notes: In order to de-blend the two shot records, firstly, we sort all the data into another domain, be it a common-midpoint, common-offset or other domain. Key point being, we sort the data such that the events of the green shot record align; then, because of the dithering of the shot times, the events of the orange shot record dis-align and appear as noise.
We strongly de-noise and assign remaining coherent energy to the green shot.
That coherent energy is removed from the original shot record.
Next, the remaining data are re-sorted such that the events of the orange shot record align; then, because of the dithering of the shot times, the events of the green shot record dis-align and appear as noise.
We strongly de-noise and assign remaining coherent energy to the orange shot.
This process is repeated several times, possibly in other domains, possibly with different de-noising tools.

## Slide 9: De-Blending
“blended” = continuous
shot record
other domain
noise model
subtracted
noise model
Notes: In order to de-blend the two shot records, firstly, we sort all the data into another domain, be it a common-midpoint, common-offset or other domain. Key point being, we sort the data such that the events of the green shot record align; then, because of the dithering of the shot times, the events of the orange shot record dis-align and appear as noise.
We strongly de-noise and assign remaining coherent energy to the green shot.
That coherent energy is removed from the original shot record.
Next, the remaining data are re-sorted such that the events of the orange shot record align; then, because of the dithering of the shot times, the events of the green shot record dis-align and appear as noise.
We strongly de-noise and assign remaining coherent energy to the orange shot.
This process is repeated several times, possibly in other domains, possibly with different de-noising tools.

## Slide 10: De-Blending
“blended” = continuous
shot record
other domain
noise shot
re-aligned
Cadzow
filtered
noise shot
noise model
updated
target shot
aligned
Notes: In order to de-blend the two shot records, firstly, we sort all the data into another domain, be it a common-midpoint, common-offset or other domain. Key point being, we sort the data such that the events of the green shot record align; then, because of the dithering of the shot times, the events of the orange shot record dis-align and appear as noise.
We strongly de-noise and assign remaining coherent energy to the green shot.
That coherent energy is removed from the original shot record.
Next, the remaining data are re-sorted such that the events of the orange shot record align; then, because of the dithering of the shot times, the events of the green shot record dis-align and appear as noise.
We strongly de-noise and assign remaining coherent energy to the orange shot.
This process is repeated several times, possibly in other domains, possibly with different de-noising tools.

## Slide 11: De-Blending
“blended” = continuous
shot record
other domain
noise shot
re-aligned
Cadzow
filtered
noise shot
noise model
updated
noise model
subtracted
Notes: In order to de-blend the two shot records, firstly, we sort all the data into another domain, be it a common-midpoint, common-offset or other domain. Key point being, we sort the data such that the events of the green shot record align; then, because of the dithering of the shot times, the events of the orange shot record dis-align and appear as noise.
We strongly de-noise and assign remaining coherent energy to the green shot.
That coherent energy is removed from the original shot record.
Next, the remaining data are re-sorted such that the events of the orange shot record align; then, because of the dithering of the shot times, the events of the green shot record dis-align and appear as noise.
We strongly de-noise and assign remaining coherent energy to the orange shot.
This process is repeated several times, possibly in other domains, possibly with different de-noising tools.

## Slide 12: De-Blending
“blended” = continuous
shot record
other domain
s
h
o
t
s
d
i
t
h
e
r
e
d
Notes: In order to de-blend the two shot records, firstly, we sort all the data into another domain, be it a common-midpoint, common-offset or other domain. Key point being, we sort the data such that the events of the green shot record align; then, because of the dithering of the shot times, the events of the orange shot record dis-align and appear as noise.
We strongly de-noise and assign remaining coherent energy to the green shot.
That coherent energy is removed from the original shot record.
Next, the remaining data are re-sorted such that the events of the orange shot record align; then, because of the dithering of the shot times, the events of the green shot record dis-align and appear as noise.
We strongly de-noise and assign remaining coherent energy to the orange shot.
This process is repeated several times, possibly in other domains, possibly with different de-noising tools.

## Slide 13: De-Blending

## Slide 14: Fieldtest: Peak Pressure
Chart: refill time [s]
| 30 | 5 | 30 | 30 | 30 | 30 | 30 | 30 | 30 | 30 | 30 | 10 | 10 | 10 | 10 | 10 | 10 | 10 | 10 | 10 | 10 | 10 | 10 | 10 | 10 | 10 | 10 | 10 | 10 | 10 | 10 | 9.5 | 9.5 | 9.5 | 9.5 | 9.5 | 9.5 | 9.5 | 9.5 | 9.5 | 9.5 | 9.5 | 9.5 | 9.5 | 9.5 | 9.5 | 9.5 | 9.5 | 9.5 | 9.5 | 9.5 | 9 | 9 | 9 | 9 | 9 | 9 | 9 | 9 | 9 | 9 | 9 | 9 | 9 | 9 | 9 | 9 | 9 | 9 | 9 | 9 | 8.5 | 8.5 | 8.5 | 8.5 | 8.5 | 8.5 | 8.5 | 8.5 | 8.5 | 8.5 | 8.5 | 8.5 | 8.5 | 8.5 | 8.5 | 8.5 | 8.5 | 8.5 | 8.5 | 8.5 | 8 | 8 | 8 | 8 | 8 | 8 | 8 | 8 | 8 | 8 | 8 | 8 | 8 | 8 | 8 | 8 | 8 | 8 | 8 | 8 | 7.5 | 7.5 | 7.5 | 7.5 | 7.5 | 7.5 | 7.5 | 7.5 | 7.5 | 7.5 | 7.5 | 7.5 | 7.5 | 7.5 | 7.5 | 7.5 | 7.5 | 7.5 | 7.5 | 7.5 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 6.5 | 6.5 | 6.5 | 6.5 | 6.5 | 6.5 | 6.5 | 6.5 | 6.5 | 6.5 | 6.5 | 6.5 | 6.5 | 6.5 | 6.5 | 6.5 | 6.5 | 6.5 | 6.5 | 6.5 | 6 | 6 | 6 | 6 | 6 | 6 | 6 | 6 | 6 | 6 | 6 | 6 | 6 | 6 | 6 | 6 | 6 | 6 | 6 | 6
Y-Values | 49.1 | 49.1 | 49 | 49.1 | 48.5 | 48.5 | 48.7 | 48.4 | 48.4 | 48.4 | 48.4 | 48.3 | 48.4 | 48.2 | 48.3 | 48.3 | 48.1 | 48.1 | 48.1 | 47.8 | 47.9 | 47.9 | 47.8 | 47.6 | 47.8 | 47.3 | 47.4 | 47.4 | 47.1 | 47.2 | 46.9
nominal

## Slide 15: Fieldtest: Peak-to-Trough Pressure
Chart: refill time [s]
| 30 | 5 | 30 | 30 | 30 | 30 | 30 | 30 | 30 | 30 | 30 | 10 | 10 | 10 | 10 | 10 | 10 | 10 | 10 | 10 | 10 | 10 | 10 | 10 | 10 | 10 | 10 | 10 | 10 | 10 | 10 | 9.5 | 9.5 | 9.5 | 9.5 | 9.5 | 9.5 | 9.5 | 9.5 | 9.5 | 9.5 | 9.5 | 9.5 | 9.5 | 9.5 | 9.5 | 9.5 | 9.5 | 9.5 | 9.5 | 9.5 | 9 | 9 | 9 | 9 | 9 | 9 | 9 | 9 | 9 | 9 | 9 | 9 | 9 | 9 | 9 | 9 | 9 | 9 | 9 | 9 | 8.5 | 8.5 | 8.5 | 8.5 | 8.5 | 8.5 | 8.5 | 8.5 | 8.5 | 8.5 | 8.5 | 8.5 | 8.5 | 8.5 | 8.5 | 8.5 | 8.5 | 8.5 | 8.5 | 8.5 | 8 | 8 | 8 | 8 | 8 | 8 | 8 | 8 | 8 | 8 | 8 | 8 | 8 | 8 | 8 | 8 | 8 | 8 | 8 | 8 | 7.5 | 7.5 | 7.5 | 7.5 | 7.5 | 7.5 | 7.5 | 7.5 | 7.5 | 7.5 | 7.5 | 7.5 | 7.5 | 7.5 | 7.5 | 7.5 | 7.5 | 7.5 | 7.5 | 7.5 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 6.5 | 6.5 | 6.5 | 6.5 | 6.5 | 6.5 | 6.5 | 6.5 | 6.5 | 6.5 | 6.5 | 6.5 | 6.5 | 6.5 | 6.5 | 6.5 | 6.5 | 6.5 | 6.5 | 6.5 | 6 | 6 | 6 | 6 | 6 | 6 | 6 | 6 | 6 | 6 | 6 | 6 | 6 | 6 | 6 | 6 | 6 | 6 | 6 | 6
Y-Values | 106.8 | 106.8 | 106.5 | 106.8 | 105.5 | 105.6 | 105.9 | 105.4 | 105.5 | 105.5 | 105.3 | 105.2 | 105.3 | 104.9 | 105.2 | 105.1 | 104.8 | 104.8 | 104.8 | 104.2 | 104.3 | 104.5 | 104.1 | 103.8 | 104.1 | 103.1 | 103.3 | 103.3 | 102.8 | 102.9 | 102.4
nominal

## Slide 16: Fieldtest: Peak-to-Bubble Ratio
Chart: refill time [s]
| 30 | 5 | 30 | 30 | 30 | 30 | 30 | 30 | 30 | 30 | 30 | 10 | 10 | 10 | 10 | 10 | 10 | 10 | 10 | 10 | 10 | 10 | 10 | 10 | 10 | 10 | 10 | 10 | 10 | 10 | 10 | 9.5 | 9.5 | 9.5 | 9.5 | 9.5 | 9.5 | 9.5 | 9.5 | 9.5 | 9.5 | 9.5 | 9.5 | 9.5 | 9.5 | 9.5 | 9.5 | 9.5 | 9.5 | 9.5 | 9.5 | 9 | 9 | 9 | 9 | 9 | 9 | 9 | 9 | 9 | 9 | 9 | 9 | 9 | 9 | 9 | 9 | 9 | 9 | 9 | 9 | 8.5 | 8.5 | 8.5 | 8.5 | 8.5 | 8.5 | 8.5 | 8.5 | 8.5 | 8.5 | 8.5 | 8.5 | 8.5 | 8.5 | 8.5 | 8.5 | 8.5 | 8.5 | 8.5 | 8.5 | 8 | 8 | 8 | 8 | 8 | 8 | 8 | 8 | 8 | 8 | 8 | 8 | 8 | 8 | 8 | 8 | 8 | 8 | 8 | 8 | 7.5 | 7.5 | 7.5 | 7.5 | 7.5 | 7.5 | 7.5 | 7.5 | 7.5 | 7.5 | 7.5 | 7.5 | 7.5 | 7.5 | 7.5 | 7.5 | 7.5 | 7.5 | 7.5 | 7.5 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 6.5 | 6.5 | 6.5 | 6.5 | 6.5 | 6.5 | 6.5 | 6.5 | 6.5 | 6.5 | 6.5 | 6.5 | 6.5 | 6.5 | 6.5 | 6.5 | 6.5 | 6.5 | 6.5 | 6.5 | 6 | 6 | 6 | 6 | 6 | 6 | 6 | 6 | 6 | 6 | 6 | 6 | 6 | 6 | 6 | 6 | 6 | 6 | 6 | 6
Y-Values | 24.8 | 24.8 | 24.6 | 24.7 | 23.8 | 23.6 | 24.5 | 23.3 | 23.4 | 23.4 | 23.4 | 23 | 23.3 | 22.9 | 23 | 23 | 22.8 | 22.7 | 22.7 | 22.3 | 22.4 | 22.4 | 22.1 | 21.9 | 22 | 21.4 | 21.3 | 21.5 | 21.1 | 21 | 21
nominal

## Slide 17: Blended Acquisition De-Blending in Processing
too rapid a succession of shot firing
more data
to be demonstrated
novel source/streamer layouts
better image quality

## Slide 18
Case History: Capreolus 3D Survey

## Slide 19: Gas until Drilled
(Carnavon
Petroleum)

## Slide 20: AGSO Regional Line

## Slide 21
VESSELS POLARCUS ASIMA / AMANI / NAILA
SOURCE Bolt 1500-LL/1900-LLXT dual sources
Volume 3480-in³
Array/Sub-Array Seps. 50m / 7.0m
Depth 7m (+/-0.5m)
Operating Pressure 2000 psi
Shot interval 12.5m flip/flop
STREAMERS Sercel Sentinel Solid
Number x Length of Str. 12 x 8100m (Phoenix area) 12 x 9000m (Beagle/Exmouth area)
Streamer Spacing 100m
Number of Groups per Str. 648/720
Depth of Streamer 17.5m (+/- 1m)
RECORDING SYSTEM SERCEL SEAL 2,000 channels + 48 aux
Sample Rate 2 ms
Lo Cut Analog 2 Hz + Digital 2 Hz(12dB)
Recording Mode Continuous
Record Length* 12.0 sec
Format SEG-D, 8058
Media 3592 Cartridge
GRAVITY & MAGNETIC DATA (WA-480P & WA-484P)
Contractor EDCON-PRJ
Gravity meter LaCoste & Romberg Model S with AirSea System II computer controller
Magnetometer SeaSpy by Marine Magnetics
Deliverables Processed digital data (CD-ROM), Maps, Final report
Acquisition parameters

## Slide 22: De-Blending

## Slide 24: Triple Sources

## Slide 25: State-of-Art: Dual Source in Flip-Flop Mode
dual

## Slide 26: Dual versus Triple Source
shot-point interval increases
fold decreases
bad idea
  too much noise
  reduced speed uneconomical
dual
triple

## Slide 27: Enabling Triple Source
blended acquisition
  shot-point interval not constrained
Notes: So, what are we doing with the third source, then?

## Slide 28: Dual Source
1/4 streamer
separation

## Slide 29: Wide Triple Source
+1/2 more streamer spread

## Slide 30: Narrow Triple Source
1/6 streamer
separation

## Slide 31: Concept Proven
TGS West-of-Shetland | triple | 12.5 > 12.5 | simultaneous  300ms dither
TGS Europa | triple | 12.5 > 37.5 | sequential overlapping
triple
left
middle
right
(Liu et al., 2015)
TGS, West-of-Shetland survey

## Slide 32: CMP-Line Separation versus Streamer Separation
streamer separation
streamer separation
dual
triple

## Slide 33: CMP-Line Separation versus Subsurface Swath Width
dual
triple

## Slide 34: Recommendation
Deep-water survey
  10  180  10,000 with ΔCMP=30m and long offsets
  12  150  8,100 with ΔCMP=25m
Shallow-water survey
  12  75  8,100 with ΔCMP=12.5m
High-density survey
  12  75  8,100 with ΔCMP=12.5m

## Slide 35: Triple Source
equal / smaller shot-point interval = equal/better in-line fold
larger sub-surface swath width, or smaller CMP-line separation
more shot- / CMP-points (per time) more rays into the ground
proven concept
  TGS West-of-Shetland, 12.5 > 12.5, simultaneous
  TGS Barents Sea, 12.5 > 37.5, overlapping sequential

## Slide 36: Penta Sources

## Slide 37: Dual Source = 6 Airgun Strings

## Slide 38: 6 Airgun Strings Re-Configured
2 strings to 1 source
firing sequence

## Slide 39: Shotpoint Interval
3s shot-time interval
over 37.5m 56.945m penta versus 312.5m or 218.75m flip-flop dual
unlimited shot records
  less source-generated noise
3s

## Slide 40: 6 Airgun Strings Re-Configured
12.5m shot-line separation
12.5m
12.5m

## Slide 41: Far-Field Signal Inside Left+Right

## Slide 42: Far-Field Signal Left Outside+Center

## Slide 43: Source Directivity: Cross-Line Inside Left+Right

## Slide 44: Source Directivity: Cross-Line Left Outside+Center

## Slide 45: 6 Airgun Strings Re-Configured
6.25m CMP-line separation
  true, not virtual data
6.25m
12.5m
62.5m

## Slide 46: Penta Source
6.25m CMP-line separation
5 versus 2 or 3 shots per 37.5m with arbitrary record length
for shallow targets

## Slide 47: Summary
blended acquisition + de-blending in processing
  more in-line shots / more source lines
  larger sub-surface swath width smaller CMP-line separation
  higher productivity  faster turn-around more data  better data quality
proven concept
  dual source: Capreolus
  triple source: West-of-Shetland and Barents Sea; ongoing field test
  penta source: awaiting award